## Slide 1: End-to-End Performance Analysis of an Analog Radio-over-Fibre System for 5G Small Cell Fronthaul
Lilian Mutia, James Jena, David Waswa
Centre for Broadband Communication, Nelson Mandela University
6th – 10th July, 2026

## Slide 2: Presentation Outline
Motivation & Background
System Architecture
Channel Impairment Model
Results & Discussion
Conclusions & Future Work

## Slide 3: Motivation & Background
Fronthaul Transport Media Types
Fibre
(P2P, WDM, PON, WDM-PON)
Wireless
(mmWaves, microwaves, FSO, sub-THz frequencies)
Copper
(coax, twisted-pair copper)
Technical requirements:
High capacity and bandwidth
Low latency
5G mobile network architecture
Fig. 1: An overview of a 5G mobile network architecture.

## Slide 4
Subcarrier Multiplexed Intermediate Frequency-over-Fibre (SCM-IFoF)
Analog Fronthaul
Central office handles all baseband processing and generates the RF / IF waveform.
Low RAU complexity.
High spectral efficiency.
Fig. 2: SCM-IFoF architecture
SCM-IFoF
  SCM-IFoF
Balances cost and capacity
Ideal for dense small cells: supports multiple users/services on a single wavelength
Seamless hybrid transport
Scalable
Phase noise
SCM
IFoF
Combiner
Mixer
Signal Generator
Laser

## Slide 5: System Architecture
Central Office (CO)
RAU
User Equipment (UE)
Fig. 3: End-to-end schematic of the analog SCM-IFoF architecture across the CO, RAU, and UE.
LO: local oscillator, MZM: Mach-Zehnder modulator, SMF: Single mode fibre, PD: photodetector, PA: power amplifier, LNA: low noise amplifier, LPF: low pass filter, ED: envelope detection

## Slide 6: Channel Impairment Model
Optical fibre transmission
Attenuation: 0.2 dB/km
Chromatic dispersion: D = 17 ps/nm·km
Laser phase noise: 100 kHz linewidth (Wiener process model)
MZM: quadrature bias point
Photodetector noise: shot noise, thermal noise
Wireless transmission
Free space path loss:
PA at RAU: Gain = 20 dB, NF = 3 dB
LNA at receiver: Gain = 25 dB, NF = 3 dB
Additive white gaussian noise (AWGN): thermal noise at receiver
Antenna gains: Tx = Rx = 7 dBi

## Slide 7: Results & Discussion
Fig. 4: PSD of the signal (a) before and (b) after up-conversion.
(a)
(b)
13 dB

## Slide 8
(a) Ideal LO
(b) Independent LO
Fig. 5: Eye diagrams of the received signals when ideal and independent LOs are used, respectively.

## Slide 9
Fig. 6: PSD of the received SCM signals when ideal and independent LOs are used
Fig. 7: BER vs LNA gain curves when ideal and independent LOs are used.

## Slide 10: Conclusions & Future Work
Conclusions
Validated that the analog SCM-IFoF architecture is physically highly viable under ideal phase synchronization.
Un-synchronized, standalone LOs breaks phase correlation, creating a severe performance barrier driven by uncompensated phase noise.
Standard architectures require massive, power-hungry DSP at the receiver, and PLLs to counteract this specific floor, defeating the low-cost purpose of an analog small cell.
Subcarrier 3 (5 GHz / 15 GHz) exhibits the worst overall performance due to CD-induced power fading, and IMD3 products.
Future work
Model a self-homodyne architecture to see how much of this specific phase noise can be physically cancelled out without excessive DSP.
A non-uniform subcarrier grid to isolate IMD3 beats into empty guard bands.
OSSB & M-QAM for spectral efficiency.

## Slide 11
References
C. Ranaweera et al., “Optical Transport Network Design for 5G Fixed Wireless Access,” Journal of Lightwave Technology, vol. 37, no. 16, pp. 3893–3901, Aug. 2019, doi: 10.1109/JLT.2019.2921378.
A. Fayad, T. Cinkler, J. Rak, and M. Jha, “Design of Cost-Efficient Optical Fronthaul for 5G/6G Networks: An Optimization Perspective,” Sensors, vol. 22, no. 23, p. 9394, Jan. 2022, doi: 10.3390/s22239394.
S. S. Jaffer, A. Hussain, M. A. Qureshi, J. Mirza, and K. K. Qureshi, “A low cost PON-FSO based fronthaul solution for 5G CRAN architecture,” Optical Fiber Technology, vol. 63, p. 102500, May 2021, doi: 10.1016/j.yofte.2021.102500.
R. I. Rony, E. Lopez-Aguilera, and E. Garcia-Villegas, “Cost Analysis of 5G Fronthaul Networks Through Functional Splits at the PHY Layer in a Capacity and Cost Limited Scenario,” IEEE Access, vol. 9, pp. 8733–8750, 2021, doi: 10.1109/ACCESS.2021.3049636.
A. Hilt, “Microwave Hop-Length and Availability Targets for the 5G Mobile Backhaul,” in 2019 42nd International Conference on Telecommunications and Signal Processing (TSP), Jul. 2019, pp. 187–190. doi: 10.1109/TSP.2019.8768870.
M. Jiang et al., “Wireless Fronthaul for 5G and Future Radio Access Networks: Challenges and Enabling Technologies,” IEEE Wireless Communications, vol. 29, no. 2, pp. 108–114, Apr. 2022, doi: 10.1109/MWC.003.2100482.
I. A. Alimi, A. L. Teixeira, and P. P. Monteiro, “Toward an Efficient C-RAN Optical Fronthaul for the Future Networks: A Tutorial on Technologies, Requirements, Challenges, and Solutions,” IEEE Communications Surveys & Tutorials, vol. 20, no. 1, pp. 708–769, 2018, doi: 10.1109/COMST.2017.2773462.

## Slide 12
Thank You!
… questions?
Change the World