## Slide 1: DEVELOPMENT OF A REMOTE, SELF-SUSTAINED, LOW-COST, LOW-POWER GNSS RTK BASE STATION FOR CONTINUOUSLY OPERATING REFERENCE STATION (CORS) NETWORKS
Presenter: Mbhasobhi Manqele
Degree: MSc in Space Science
Institution: University of KwaZulu-Natal (UKZN)
Supervisors: Prof. Riaan Stopforth (UKZN) & Prof. Michael Kosch (SANSA)
07 July, 2026.

## Slide 2
2
OUTLINE
Introduction
Methodology
GNSS fundamentals
RTK & CORS concept
GNSS receiver selection
System design and implementation
RINEX
Testing and evaluation
Contribution and future work

## Slide 3
3
INTRODUCTION
Why a Low-Cost CORS Station?
Professional GNSS reference stations with high accuracy are expensive & difficult to deploy (slide 3)
Low-cost dual-frequency GNSS receivers now provide Raw observations, Multi-constellation capability, and RTCM output.
Impact Areas:
Precision agriculture, Surveying and infrastructure development, Geodetic research, and Space weather monitoring
Objectives:
Design, integrate, and deploy a working prototype of a low-cost hardware system.
A system that delivers GNSS data to a centralized server based at SANSA
Evaluate the performance of the GNSS prototype in terms of data quality
Estimate TEC capability

## Slide 4
4
RESEARCH METHODOLOGY
Literature Review
Requirement Analysis
Hardware Development
Software Integration
Field Testing
Performance Evaluation
Establish the theoretical foundation required for GNSS RTK and CORS station development.
Identified the technical requirements for a low-cost scientific GNSS reference station.
Design specifications
Translate research objectives and operational requirements into measurable system specifications.

## Slide 5
5
GNSS FUNDAMENTALS
GLOBAL NAVIGATION SATELLITE SYSTEMS (GNSS)
Regional Systems
QZSS (Japan)
NavIC (India)
BeiDou
(China)
Galileo
(EU)
GPS
(USA)
GLONASS
(Russia)
~31
~28
~24
~30
Global satellite (18-30 operational satellites)
Contents of the GNSS signals:
Carrier wave
Pseudo-Random Noise (PRN) code
Navigation Message

## Slide 6
6
Feature | Low-Cost Receiver (u-blox ZED-F9P) | High-Grade Receiver
Cost | ~R4,000–R6,000 | R80,000–R300,000+
Power Consumption | < 1 W | 3–10 W
Size & Weight | Compact and lightweight | Larger and heavier
GNSS Constellations | GPS, Galileo, GLONASS, BeiDou | All major constellations
Multi-frequency Support | Dual-frequency (L1/L2/E5b/B2I) | Multi-frequency (L1, L2, L5, E5, E6, etc.)
RTK Positioning | ✔ Centimeter-level | ✔ Survey-grade centimetre-level
Raw Data Output | UBX, RTCM, RINEX | SBF, RTCM, RINEX
Real-time Streaming | ✔ RTCM MSM7 | ✔ RTCM MSM7
Ionospheric Monitoring | ✔ Suitable for TEC estimation | ✔ Scientific-grade
Scintillation Monitoring | Possible through post-processing | Often includes dedicated scintillation capabilities
Internal Storage | Limited | Large internal memory
Environmental Protection | Requires external enclosure | Rugged industrial enclosure
Intended Application | Low-cost CORS, UAVs, Robotics, Research | National CORS, Geodesy, Scientific Observatories
LOW-COST GNSS RECEIVER VS HIGH-GRADE GEODETIC GNSS RECEIVER

## Slide 7
7
RTK AND CORS CONCEPT
Achieving Centimeter-Level Positioning
RTK principle:
A fixed base station provides correction data
Rover receiver applies corrections
Common GNSS errors are reduced
CORS network:
Permanent RTK reference stations
Continuously collect GNSS observations
Provide corrections through communication networks
NTRIP communication:
Standard protocol for transmitting RTCM corrections over the internet
Figure 1: GNSS RTK Base (left) and Rover (right)

## Slide 8
8
GNSS RECEIVER SELECTION
ZED-F9P:
Affordable & Low power consumption
Dual-frequency GNSS capability
Multi-constellation support
RTCM MSM7 output
Suitable for autonomous CORS
Septentrio mosaic-X5:
High accuracy
Multi-frequency GNSS tracking
Professional grade
Scientific benchmark
Suitable for:
Geodesy
Atmospheric monitoring
Space weather research
Permanent GNSS networks
U-blox ZED-F9P
SparkFun GNSS Flex pHAT
Mosaic-X5 GNSS pHAT

## Slide 9
9
COMPONENTS
Raspberry Pi 4
GNSS Antenna
LiFePO4 Battery Pack
ZED-F9P
Solar Panel
UPS module+RPi
MPPT Charge controllers
UPS Module

## Slide 10
10
SYSTEM ARCHITECTURE
GNSS Satellite – GPS.GLONASS.Galileo.BeiDou
GNSS Antenna
u-blox ANN-MB-00
U-blox ZED-F9P
RTCM 3.3 MSM7 output
Sensing
Raspberry Pi 4 (8GB)
Streaming & logging host
Computer
RINEX 3 logging
RINEX files
NTRIP
Streams RTCM MSM7
Communications
Local storage
Solar panel
100W panel
MPPT controllers
Charge regulation
Battery & UPS
3-5 day autonomy
Power

## Slide 11
11
RINEX: THE STANDARD FORMAT FOR SCIENTIFIC GNSS DATA
Receiver Independent Exchange Format (RINEX)
International standard for storing & exchanging raw GNSS observations
Supports precise positioning and ionospheric research
Information Stored
Pseudorange, Carrier phase, Doppler & Signal strength
Satellite Signals
ZED-F9P
RINEX Obs. files
UBX Binary
Scientific Processing
FTP Server
.UBX
SBF
TEC+S4+SigmaPhi (approx.)
RINEX files
Conversion script
RINEX/ISMR
TEC+S4+SigmaPhi
Conversion
formats
ZED-F9P:
Mosaic-X5
Logging script
Receiving GNSS Data

## Slide 12
12
TESTING: PROTOTYPE HARDWARE INTEGRATION
Figure 1: u-blox ZED-F9P
Figure 2: Septentrio Mosaic-X5
Hardware Assembly
Raspberry Pi 4 is used as the embedded processing platform.
Real-time GNSS observations monitored using PyGPSClient.
Purpose for Testing before deployment
Enable SSH for remote monitoring
Confirm receiver communication with the Raspberry Pi.
Test data acquisition workflow.
Identify hardware or communication issues before deployment.
Ensure stable operation for autonomous field use.

## Slide 13
TESTING: REAL-TIME GNSS DATA ACQUISITION
PyGPSClient Window
Data Logging
The ZED-F9P GNSS receiver is connected
Receiving live satellite signals
Decoding multiple GNSS constellations
Displaying the observations in PyGPSClient.
UBX provides: raw measurements, carrier phase, pseudorange, Doppler, receiver status
Used for:
RINEX generation, TEC estimation & scientific processing
13

## Slide 14
14
TESTING: AUTOMATIC COMPUTATION
RINEX files
Satellite Data
The system is doing more than simply collecting GNSS data.
Processing the raw observations into ionospheric scintillation parameters,
The primary scientific objectives of your project.
Automatically converting and archiving binary files into standard RINEX files.
A directory on the Raspberry Pi where the automatically generated RINEX files are stored

## Slide 15
15
TESTING: RAW GNSS DATA LIVE MONITORING

## Slide 16
16
CONCLUSION
Successfully designed and developed a low-cost, low-power GNSS RTK base station prototype using COTS components
Demonstrated reliable multi-constellation, dual-frequency GNSS data acquisition.
Developed an autonomous software framework capable of continuous data acquisition, health monitoring, automatic file generation, local storage, and remote data transmission without user intervention.
Demonstrated the ability to compute ionospheric scintillation parameters (S4, and Sigma Phi), highlighting the prototype's capability for space weather and ionospheric monitoring.
Proposed Future Research: OrbitSense AI Platform
Extend the low-cost GNSS base station into a network of autonomous CORS stations deployed across South Africa.
Integrate multiple GNSS stations into the OrbitSense AI Platform for centralized data collection, storage, monitoring, and management.
Develop an AI-powered analytics platform capable of processing real-time GNSS observations from multiple stations simultaneously.

## Slide 17
17
……….......
_________________________
_________________________
……….......

## Slide 18
18
REFERENCES
N. Wielgocka, T. Hadas, A. Kaczmarek, and G. Marut, “Feasibility of using low-cost dual-frequency gnss receivers for land surveying,” Sensors, vol. 21, no. 6, p. 1956, 2021.
V. Hamza, B. Stopar, and O. Sterle, “Testing the performance of multi-frequency low-cost gnss receivers and antennas,” Sensors, vol. 21, no. 6, p. 2029, 2021