## Slide 1
Design and Implementation of a Modular Telescope and Dome Control System (TelServer)
www.ufs.ac.za
HJ van Heerden
70th Annual Conference of SAIP
July 2026

## Slide 2
Project Aim: To research, design and implement upgraded systems and platforms for the 1.5m Boyden Reflector for full remote and semi-autonomous use utilizing the SAAO IO approach for operational effectiveness.
Introduction
Telescope project and TelServer
July 2026

## Slide 3
Telescope Control
Dome Control
Science Instruments
Guiding systems
Environment
Network and Data systems
Project Components
Telescope project and TelServer
July 2026

## Slide 4
Introduction
Telescope project and TelServer
July 2026

## Slide 5
What is TelServer
Telescope project and TelServer
July 2026
Integrates telescope and dome control into a unified framework
Interfaces with DFM Telescope Control System (RS232)
Controls dome rotation and shutters via PLCs
Socket-based architecture supports multiple clients:
  Python scripts, Web interfaces or C/C++ applications
Hardware abstraction separates control logic from device interfaces
Standardized APIs for:
  Telescope pointing, Dome rotation and Shutter control
Scalable, flexible, and extensible system architecture

## Slide 6
Telescope project and TelServer
July 2026

## Slide 7
1. UI sends observation, telescope, dome, and imaging commands to TelServer through the TCP/IP API.
2. TelServer validates requests, coordinates system state, and issues control commands.
3. TelServer controls the DFM Telescope via RS232 and continuously receives position, status, and telemetry.
4. TelServer communicates with the Dome Control PLC via TCP/IP to operate dome rotation, shutters, lighting, and safety systems.
5. The UI initiates image acquisition on the Camera/Guider PC using CamServer or pyObs over Ethernet.
6. Science and guider images are written directly to the central TrueNAS storage via an NFS share.
7. The UI accesses guider images from the same NFS storage for real-time processing.
8. Local Astrometry.net performs plate solving to determine the true telescope pointing.
9. Guide star tracking measures centroid motion to determine tracking errors.
10. Telescope position, timestamps, and telemetry logged by TelServer are correlated with each acquired image.
11. Measured tracking and pointing errors are compared with the expected telescope position.
12. Model-learning algorithms estimate corrections for telescope pointing and tracking models.
13. The updated corrections are sent back to TelServer through the TCP/IP API.
14. TelServer applies the refined pointing and tracking corrections, closing the feedback loop for future observations.
Standard control flow
Telescope project and TelServer
July 2026

## Slide 8
Telescope project and TelServer
July 2026

## Slide 9
Telescope project and TelServer
July 2026

## Slide 10
Introduction
Telescope project and TelServer
July 2026

## Slide 11
Introduction
Telescope project and TelServer
July 2026

## Slide 12
Introduction
Telescope project and TelServer
July 2026

## Slide 13
Introduction
Telescope project and TelServer
July 2026

## Slide 14
Introduction
Telescope project and TelServer
July 2026

## Slide 15
Telescope project and TelServer
July 2026

## Slide 16
Telescope dust cover controls
Telescope focus position encoder
Environmental – Weather station
Finalize network upgrades
Upgrade telescope DFM system to PLC system.
And etc…
Still need to happen
Telescope project and TelServer
July 2026

## Slide 17
T: +27(0)51 401 3509 І vanheerdenhj@ufs.ac.za І www.ufs.ac.za
This work is based on the research supported by the Department of Science and Innovation and the National Research Foundation of South Africa.
Thank You
Dankie